## Slide 1: PR for rev0.5 feedback

## Slide 2: Stepie
Current | Feedback in PR
DCSR.stepie in only configurable when mdbgen is 1 It disables all interrupts when stepie=0 | DCSR.stepie is always configurable in Debug Mode It disables the interrupts delegated to debug-allowed privilege (e.g. interrupts trap to M-mode is not affected when mdbgen is 0)
Notes
Everyone agreed on the right side

## Slide 3: Abstract command, Quick Access
Current | Feedback in PR
Abstract Command without halting, Quick Access return error when debug is not allowed | They should be pending until debug is allowed
Notes
Quick Access implies halt request, so should be aligned to halt behavior (wait-until-allow)
The right side might be problematic to abstract command
  Halt is non blocking, abstract command is blocking, an abstract command may hang debugger
  No conclusion, plan to follow up offline in the mailing list

## Slide 4: Halt-on-reset
Current | Feedback in PR
Raise error when mdbgen is 0 as reset is de-asserted Debug at the very first instruction, otherwise indicates error | Halt will be pending until debug is allowed Debug at the first debuggable instruction
Notes
Everyone agreed on the right side

## Slide 5: aamvirtual
Current | Feedback in PR
Hardwired to 1 to enforce virtual address | Honors the mstatus.TVM. When TVM=1, access with aamvirtual=0 returns 0 and set cmderr to 3 (excpetion)
Notes
There’s a misunderstanding in this description. TVM does not enforce virtual addressing
All agreed that aamvirtual shall follow the same requirements that apply to debug privilege
  Debugger will not return error when setting aamvirtual
  Hart will raise exception on illegal access

## Slide 6: Sticky error status
Current | Feedback in PR
Allsecfault/anysecfault indicates the error for latest operation. | Allsecfault/anysecfault shows the earliest error Error cleared by acksecfault introduced in dmcs2
Notes
Agreed on the right side

## Slide 7: All rule check happens at hart side
Current | Feedback in PR
Rule check happens both at hart and DM side | Rule check happens only at hart side
Notes
Need to decide case by case, but hard to eliminate check at DM side
  e.g. ndmreset is not related to hart