## Slide 1: RISC-V External Debug Security TG
Meeting notes – 11/15/2023

## Slide 2: Disclaimer
https://docs.google.com/presentation/d/1LNhpuNwU54TgwGfcl-Fgf4HUFxCxh0AztPaeqMuRQRw/edit#slide=id.p1

## Slide 3: Agenda
Introduction
Review TG charter
Goal for Nov
Discuss arch opens

## Slide 4: Introduction
Acting chair – Joe Xie @nVidia
Acting vice-chair – Gokhan Kaplayan @Imgtec
Contributor - Aote Jin @nVidia
Enrico @Intel
Beeman @Rivos
Robert @Individual
Paul @Ventana
Erick @NXP
Yann @SiFive
Vicky @IMG

## Slide 5: TG Charter Review (No Change)
TG Charter Draft
Status
  Had two rounds of reviews with related SiG/HC (RTI, DTPM, SOC, Security)
Last changes
  Include trace spec to the scope for TG
  Make authentication mechanism future considerations (originally out-of-scope)
Notes: extended for RISC-V Trace Control Interface Specification

## Slide 6: Goal for Nov
TG
  Get TSC to review and approve TG charter
  TG chair and vice-chair ellection
Spec (https://github.com/joxie/riscv-debug-security/blob/main/spec/Secure%20Debug%20Proposal.md)
  Create ratification plan and status checklist
  Create spec github repo, and move proposal draft to offical spec github repo
Notes: AI – Joe to Provide link to the existing draft in the notes

## Slide 7: Dev Spec Status (Aote)
Keepalive should be either ignored for all debug privilege levels or at least for sub-machine mode privilege levels.
Relaxedpriv must be hardwired to 0x0
The fields in dcsr require sufficient privilege level to access, otherwise the fields will be masked by 0x0 (mutiplexed to read-only zero if privilege not suffice and switched back to be configurable fields if granted sufficient privilege).
Debug PC (dpc) and Debug Scratch Register (dscratch0, dscratch1)The CSR dpc, dscratch0 and dscratch1 is accessible when the hart enter a debuggable privilege level.
Triggers with action = 1 (enter debug mode) will only match/fire if debug is enabled for the privilege level where the hart hits the trigger.
In debug mode:
  - triggers (action = 0/1) cannot be enabled for privilege levels higher than the one specified in mdbgsec.dbgprv/mdbgsec.dbgv.
  - triggers (action = 2/3/4) cannot be enabled for privilege levels higher than the one specified in mdbgsec.trcprv/mdbgsec.trcv.
  - triggers (action = 8/9) cannot be enabled if mdbgsec.extrigdis is zero.
Notes: Async trigger from mode with debug disabled may hit after priv mode change and match in another mode, this can be used as a weapon to attack higher privledge mode. Mandate implementation.
Triggers in a mode that disables debug (sync vs async, pending bit)
The between debug enable and authentcation mechanism for example authentication is set but debug is disabled.
Clarify system relationshipbus protections (WG / IOPMP or similar checker mechanism), put that on the list for next stage discussion.
ARMv8M debug solution – take a look into the M mode isolation spec and how does this interact with debug security.

## Slide 8: Arch Opens & Issues
https://github.com/joxie/riscv-debug-security/blob/main/spec/Secure%20Debug%20Proposal.md
External Trigger of Core Trigger Module

## Slide 9: Meeting notes and Actions
Charter discussion
  Joe / Gokhan to start offical approval process right now, don’t have to wait
Spec (https://github.com/joxie/riscv-debug-security/blob/main/spec/Secure%20Debug%20Proposal.md)
  Async triggers can be weaponized by low priv mode to attack high priv mode
    AI – Aote to open a new issue – Aote
  How to handle trigger match when debug is disabled
    https://github.com/riscv-admin/external-debug-security/issues/2
  Clarify the relationship between debug enable and authentication bits
    AI – Aote to open an issue
  Clarify system protections (WG / IOPMP or similar checker mechanism)
    Open a new issue
    https://compass.sustech.edu.cn/nailgun/ (ARM nailgun attack, we should provide some guidance to help implementation to avoid such kind of attack in RISC-V world)
  How does debug security spec interact with m-mode isolation extension?
    AI – Aote to check M mode isolation spec

## Slide 10: Backup Slides