## Slide 1: RISC-V External Debug Security TG
Meeting notes – 1/15/2024

## Slide 2: Disclaimer
https://docs.google.com/presentation/d/1LNhpuNwU54TgwGfcl-Fgf4HUFxCxh0AztPaeqMuRQRw/edit#slide=id.p1

## Slide 3: Agenda
TG update
Arch opens

## Slide 4: Introduction
Welcome to TG meeting
Feel free to raise your hand and introduce yourself

## Slide 5: New meeting time
Tuesday 3pm, every other week from 1/30 (NOT Monday)

## Slide 6: Spec Repo
Official repo created https://github.com/riscv-non-isa/riscv-external-debug-security
Plan to move proposal from https://github.com/joxie/riscv-debug-security to offical repo in the next two weeks

## Slide 7: Extension Management
ISA extension
  https://github.com/riscv/riscv-smmtt
Non-ISA extension
  https://github.com/riscv-non-isa/riscv-external-debug-security

## Slide 8: Arch Opens
Aote Jin

## Slide 9: (Potential) Privilege escalation issue

## Slide 10: Cont’d
What is the concern?
  Debugger grants higher privilege level
  To debug U mode domain, debugger grants S priv. level
Is this a real threat?
  Need more research and (potentially) PoC
  Read Perf counter, manipulate timer/interrupt
  Modify page table to compromise other domain*
Solution space?
  (Arch) Add an optional nob to regulate U-mode debug?
  (SW) Enclave model SW to create S mode layer to provide self-host debug service
* - PMP can be used to mitigate this threat, but PMP entries are precious

## Slide 11: Toctou issue
The Issue
  The logic to check haltreq might be far away from the hart
  Debug control check passes, but hart changes to a undebuggable privilege mode when haltreq arrives hart
Mitigation
  Implementations to guarantee?
    No privilege change during trigger firing/matching
    Haltreq check logic close to the hart

## Slide 12: Proposal to mitigate
Implementation must assure no privilege change between the debug control check and serving the debug request
  E.g. implement the debug control logic close to hart or inside the hart
Mandate that no privilege change during trigger firing/matching

## Slide 13: Backward compatibility
Option 1: not back compatible
  Debugger polling alledsec/anyedsec in dmstatus to determine whether External Debug Security extension is available in hart
  If available, the debug operation will be different
    Need to program dcsr to get M-mode accessibility
Option 2: partially back compatible when M-mode is debugable
  When M-mode is debuggable, hart behaves as no External Debug Security
  Relaxedpriv still hardwired to 0x0
  System Bus Access still honors bus initiator protection e.g. IOPMP

## Slide 14: External trigger privilege control
External trigger missing M/S/VS/VU enable bits in tmexttrigger
  S-mode debugger might attack M-mode by external trigger (e.g. DoS, side channel)
External trigger inputs might have resource belongs to M-mode
  Since M-Mode is enabled by RoT, external triggers should be enabled by RoT as well

## Slide 15: Proposal to mitigate
Add per privilege enable bits like other triggers
Mandate that external trigger shall only be enabled by RoT and lockable

## Slide 16: Defeature ndmreset
Ndmreset is a system level reset which is not associated with hart privilege and can only be protected by system; thus it shall be defeatured.

## Slide 17: Keystone

## Slide 18: Smmtt

## Slide 20: Notes
Priv escalation
  Need more info to decide between spec fix vs SW mitigation
  NXP already introduced customized u-mode debug control
  AI – Joe to check with Penglai people
  AI - Aote to update original issue with the new findings (https://github.com/riscv/riscv-smmtt/issues/11)
TocTou issue
  Prefer to update diagram, move haltreq checker loggic into hart
  AI – Aote to create a new issue in Smmtt repo
Backcompatiblity issue
  AI – Joe to check with debugger SW guys

## Slide 21: Backup Slides